## Slide 1
C. J. Lee
Office of Biometric Identity Management (OBIM)
DNA Fragment Sequence Analysis (FSA) Data File Format Standard
2022
Notes: Briefing on the data format standard for DNA fragment sequence analysis (fsa)

## Slide 2: What is DNA fsa data
DNA fragment sequence analysis (fsa) data is an output of the capillary electrophoresis (CE) instruments, commonly used in forensic DNA testing worldwide for producing sharable DNA profiles.
DNA data shared between organizations mainly contain the Short Tandem Repeat (STR) allele calls based on the DNA fsa data.
DNA fsa data is often called “the raw DNA data” and is included in the ISO/IEC and NIEM DNA schema as a Base64 encoded binary data block. There is no format standard on the content of the DNA raw data.

## Slide 3: DNA fsa data and standard
DNA hardware and software vendors have been using the Applied Biosystems (ABI) Genetic Analysis Data File Format (2009), also known as the "fsa" file, to share DNA raw data.
ABI 2009 format specification is outdated and cannot support any DNA peak height value larger than a 16-bit integer (32,767).
A standard for the DNA fsa data is needed to facilitate
  Rapid DNA crime scene technology advancement
  Data sharing between DNA instruments and analysis tools
Members of the NIEM Biometrics Domain Working Group (NBDWG), consisting of law-enforcement organizations, DNA hardware and software vendors, recommended in November 2020 to establish a standard DNA fsa data format, extending from the existing ABI 2009 format; and maintain the standard in the public domain with a mechanism to submit, approve and implement change requests.
Notes: The ABI 2009 format is modeled mainly after the Tag Image File Format (TIFF), a format for graphics files.
DNA hardware vendors have been adding custom tags in the fsa files, making different undocumented versions of fsa files for each instrument model and data collection software version
A standard for the DNA fsa data will meet Requirement #2 outlined in the agreed position statement by ENFSI, SWGDAM and the Rapid DNA Crime Scene Technology Advancement Task Group (2020): Rapid DNA instruments must be able to export analyzable raw (optical preprocessed) data.

## Slide 4: DNA fsax open-source project
A draft standard, the extended DNA fsa data format, also known as the “fsax” format was developed in 2021 based on the ABI 2009 format
In addition to the 2009 content, fsax combined all existing custom data tags so that the existing fsa implementations should be automatically compliant with the standard
DNA fsax specification is posted on the NIEM GitHub site NIEM-Biometrics-Domain-DNA-Analysis
DNA fsax specification has been reviewed by the community SMEs from the DHS, FBI, NIH, hardware vendors and software vendors
Notes: fsax combined the data tags produced by
  ABI PRISM 3100, 3100-Avant Genetic Analyzer / Data Collection Software v2.0
  ABI 3130/3130xl Genetic Analyzer / Data Collection Software v3.0
  ABI 3500/3500xl Genetic Analyzer / Data Collection Software v1.0
  ABI 3730/3730xl DNA Analyzer / Data Collection Software v2.0
  ABI 3730/3730xl DNA Analyzer / Data Collection Software v3.0
DNA fsax specification is reviewed by the community SMEs from
  ANDE
  Cybergenetics
  DHS OBIM
  FBI CODIS Unit
  NIH NLM NCBI
  Promega Spectrum CE/Hitachi High Tech
  SoftGenetics
  Thermo Fisher Scientific

## Slide 5: Moving forward
FBI suggested to obtain feedback from the SMEs and administrators at the state and local crime laboratories, especially for the versioning and release process of the updated DNA fsa data format standard
Publish the official first version of fsax specification to the community using the NIEM release process
Migrate to OASIS and follow the OASIS process to become one of the OASIS standards